## Slide 1: Storage for the DBA
Denny Cherry
Manager of Information Systems
mrdenny@mrdenny.com
MVP, MCSA, MCDBA, MCTS, MCITP

## Slide 2: Just to be clear …
Any Questions?

## Slide 3: Topic Highlights
Storage Arrays
Storage Networks
Virtualizing SQL Servers

## Slide 4: Storage Agenda
Storage Terminology
Array Cache Setup
RAID Types
Tiered Storage
Disk Alignment
Spindle Types
Physical Array Diagram
Array Design Differences
Snapshots, Clones
Array Based Replication
Multipath IO Drivers
Thin Luns
Monitoring
Power Up / Power Down

## Slide 5: Storage Terminology
LUN = Logical Unit Number
Host = The Server or Servers a LUN is presented to
SAN = Storage Area Network
Fabric = Network which makes up the SAN
Spindle = Physical disks in the Storage Array
Array = Box with the Spindles in it

## Slide 6: Storage Terminology
Disk = How the OS sees a LUN when presented
IOps = Physical Operation To Disk
Sequential IO = Reads or writes which are sequential on the spindle
Random IO = Reads or writes which are located at random positions on the spindle

## Slide 7: Cache Setup
OLTP databases make poor use of SAN read cache
OLAP databases make good use of SAN read cache
Try reducing read cache and increasing write cache
OLTP databases with high buffer cache hit ratios may be able to have the read cache disabled
There is no one correct setup. Every system is different.

## Slide 8: When Cache Gets Full?
Doesn’t flush to disk until low watermark is hit
Force flushes once high watermark is hit
Force flushing completely empties write cache
Force flushing disables write cache until write cache is disabled
If adjustable, set low very low, and high watermark very high (20/90)

## Slide 9: Oh crap the power went out!
Most arrays have internal batteries
Write cache is flushed to disk
After flush array powers down
On power-up flushed cached is read and committed to LUNs before LUN is made available
Make sure SQL is down before the array flushes

## Slide 10: EMC Physical Diagram

## Slide 11: Flash Cache
Being introduced by some vendors
Either EFDs or flash card used as secondary cache
High cost
High performance
Some vendors provide redundancy with cache, some don’t.
Some vendors provide for read only, some read write

## Slide 12: RAID Types
RAID 0
  Straight Stripe
  No redundancy
  Very fast
  Low cost
  Any disk failure looses data
  Can not survive no disks failures
  Requires 2 or more disks

## Slide 13: RAID Types
RAID 1
  Full Mirror of data
  No performance Benefit
  High Cost
  Requires 2 disks
  Can survive 1 disk failure

## Slide 14: RAID Types
RAID 0+1
  Drives Striped, then Stripes Mirrored
  High Cost
  High Performance
  Requires 2 disks
  Requires an even number of disks
  Can survive 1 spindle failure
  May survive multiple spindle failure

## Slide 15: RAID Types
RAID 10 (aka 1+0)
  Drives Mirrored, then Mirrors Striped
  High Cost
  High Performance
  Requires 2 disks
  Requires an even number of disks
  Can survive 1 spindle failure
  May survive multiple spindle failure

## Slide 16: RAID Types
RAID 5
  Stripe with single parity drive
  Low cost
  Good performance
  Write penalty
  Can survive a single drive failure
  Requires at least 3 disks

## Slide 17: RAID Types
RAID 6
  Stripe with two parity drives
  Slightly higher cost per gig than RAID 5, good performance
  Same write penalty as RAID 5
  Can survive 2 disk failures
  Requires at least 4 disks

## Slide 18: What’s the correct choice?
Logs, TempDB – RAID 1, 10, 0+1
System Databases – RAID 5, 6
Backups – RAID 5, 6
User Data – RAID 5
Indexes – RAID 5

## Slide 19: When to switch RAID types
From 5 to 10 (or 0+1)?
  Over 10% data change (30% on EMC storage)
  High writes
  Cache is force flushing
From 5 to 6?
  Disks fail often

## Slide 20: Tiered Storage
Time is Money
http://www.flickr.com/photos/21560098@N06/3832712784/

## Slide 21: Tiered Storage
Tier 0
  Enterprise Flash Disks low capacity drives
  Very high cost
  Very high speed storage
  Great for Databases

## Slide 22: Tiered Storage
Tier 1
  15k RPM Fibre Channel low capacity drives
  High cost, high speed storage
  Great for Databases, Exchange, Virtual Machines

## Slide 23: Tiered Storage
Tier 2
  10k RPM Fibre Channel medium capacity drives
  Medium cost, medium speed storage
  Great for File Servers, Database Archives

## Slide 24: Tiered Storage
Tier 3
  7.2/5.4k RPM SATA/SAS high capacity drives
  Low cost, low speed storage
  Great for Backups, Archives

## Slide 25: Disk Alignment
Can improve SQL disk performance up to 100%
  (64 1k blocks/64k IO)=100% of IO is impacted
Must be done before data is put on the disk
Windows 2000 - Diskpar
Windows 2003 - Diskpart
Windows 2008 - Automatic

## Slide 26: Disk Alignment

## Slide 27: Bus Speeds
Front end ports – 2-8 Gigs
  Ports the clients use to connect to the storage array
Back end ports – 1-20 Gigs
  Ports the controller uses to talk to other components within the array

## Slide 28: Spindle Types
Enterprise Flash Disks (EFDs)
  Newest Technology
  4 Gig Buss Speed
  Up to 30k IO per spindle
Fiber Channel (FC)
  2-4 Gig bus speeds
  10k-15k RPM
  Up to ~300 IO per spindle

## Slide 29: Spindle Types
SCSI
  Older Technology
  1-2 Gig Bus Speed
  Up to 200 IO per spindle
  Up to 10k RPM
SATA
  Newer Technology
  1-4 Gig buss speed
  Up to 200 IO per spindle
  7200 RPM

## Slide 30: Array Diagram

## Slide 31: Different Storage Array Design Techniques
Shared Everything (RAID 10)
Shared Everything (RAID 6)
Shared Some with Admin Control
No RAID arrays

## Slide 32: Shared Everything (RAID 10)
3PAR
Each pair of disks is a RAID 1 array
Use Lots of Disks
Data on Disks is a chunk
Create LUNs as (disks*chunk size)
One disk slows down, everything slows down
No Parity Calculations

## Slide 33: Shared Some with RAID 6
NetApp
Each shelf is a RAID 6 Array
Each write has two parity calculations
One LUN slows down, everything on the shelf slows down.
Easy to manage

## Slide 34: Shared Some Array
EMC, Hitachi, Some IBM Units
High Management Overhead
Total Control of LUN placement
LUN can span RAID groups

## Slide 35: No RAID Storage Arrays
IBM XIV
Disk shelves are either IO modules or disk modules
Data is placed on one IO module and one disk module
LUNs are created in 1 Meg chunks on as many disks are needed to create the LUN.
Can survive multiple disk failures
Can survive multiple shelf failures
If the right two disks fail, a LUN can become corrupt

## Slide 36: No RAID Storage Arrays
How the data is written

## Slide 37: Snapshots
Similar to SQL Server Snapshots
A consistent point in time snapshot on a LUN
Can be mounted to other servers in read or read/write mode
Requires that host disks be flushed before spapshot can be taken

## Slide 38: Clones
Exact duplicate of source LUN
Typically created on different physical disks

## Slide 39: Copy on First Write
Used by most arrays for snapshots
Used by VMware for snapshots
First time block is written to, old block is copied to snapshot location

## Slide 40: Copy on First Write
Data Raid Groups
Snapshot Space
Snapshot is Taken

## Slide 41: Without Consistency you’ll have egg all over your face.

## Slide 42: Consistency is Key
When taking a snapshot of LUNs hosting databases all LUNs must be consistent with each other or database will be suspect.
Requires host flushes all writes to disk, and pauses all writes while snapshot is taken.

## Slide 43: Array based replication
Techniques vary depending on array vendor
Most arrays can only replicate to same brand or series
  EMC to EMC
  IBM to IBM
  NetApp to NetApp
Can be done with synchronous or asynchronous
  Synchronous shouldn’t has a ~100 km limit

## Slide 44: MPIO Drivers
Without MPIO Drivers
http://www.flickr.com/photos/ellipse/67038205/

## Slide 45: MPIO Drivers
With MPIO Drivers
http://www.flickr.com/photos/ellipse/67038430/

## Slide 46: MPIO Drivers
Windows 2003+ includes a native MPIO driver
Native driver supports only 1 active path
Some 3rd party MPIO drivers support multiple active paths
Native driver is free, 3rd party drivers not so much

## Slide 47: Thin Luns
Allows for over committing of storage
Allocates storage as needed when needed
Allows business to request huge amounts of storage when small amounts of storage are actually needed
Pretty much pointless for databases

## Slide 48: Monitoring
Storage arrays require monitoring
Some monitoring packages are add-on modules
Host based monitoring (perfmon) isn’t giving you the whole story
Monitor RAID Group, LUN, Disks
Know which monitors are averages, which are maximums

## Slide 49: Power Up / Power Down
Power Up Sequence
Power Down Sequence
Switches
Storage Array Disks
Storage Array Controller
Servers
Servers
Storage Array Controller
Storage Array Disks
Switches

## Slide 50: Contrary to popular belief…
Not all arrays do everything well
Storage Arrays require maintenance
SANs make good NASs but NASs don’t make good SANs
Writing fast <> reading fast

## Slide 51: Storage Network Agenda
When to use iSCSI or Fibre Channel
What needs to be redundant?
Path Count
What can be Active/Active and what can’t?
When should the switches be connected together?
Calculating network latency

## Slide 52: iSCSI VS Fibre Channel
Its about choice. The same choice doesn’t work for every situation.
http://www.flickr.com/photos/randysonofrobert/385847732/

## Slide 53: What needs to be Redundant?
HBAs / iSCSI NICs
Fiber Channel Switches / Network Switches
Storage Controllers
Front End Ports Array Ports
Back End Loops

## Slide 54: Redundant Fiber Channel Network

## Slide 55: Redundant iSCSI Network

## Slide 56: Redundant iSCSI Network w/ Virtualization

## Slide 57: Path Count
Each HBA has a path to each front end port on the same switch
Each iSCSI has a path to each front end port to which connectivity is granted.

## Slide 58: Fiber Channel Paths

## Slide 59: iSCSI Paths

## Slide 60: What can be Active/Active?
Yes
No
HBAs
Switches
Array Storage Processors
Single LUN Accessed through multiple switches (sometimes)
Single LUN Accessed through multiple HBAs (sometimes)
Single LUN on multiple Storage Processors
Multiple Servers Accessing the same LUN

## Slide 61: Why Active/Active?
Greater bandwidth between server and host
4 Gig front end ports max out at 380 Mbytes / sec
8 Gig front end ports max out at 760 Mbytes / sec
Requires Active/Active MPIO driver like PowerPath on server and supporting array

## Slide 62: World Wide Name
Fiber channel equivalent of a MAC address
Every port has a WWN
WWNs can be aliased to make them readable

## Slide 63: Port Zoning
Tells the fiber switch to allow communication from one port to another
Can be done by physical ports or WWNs (or aliases)
  Physical port zoning makes replacing HBAs easier
  WWN zoning makes moving HBAs to another port easier
Most array vendors do not support single zone, zoning

## Slide 64: Port Zoning
In Windows 1 HBA is zoned to all array front end ports
In VMware 1 HBA is zoned to 1 front end ports
HBAs can be in multiple zones

## Slide 65: Connecting Switches Together
Called ISL – Inter-Switch Link
Allows equipment on one switch to access other switch
Allows for network growth without replacing equipment
Brocade/McData requires ISL License
ISL Greatly reduces port counts
ISL cables only run at ½ speed
Multiple ISL ports should be on same ASIC
Always push config to switches, then activate.
Trunk ports for increased bandwidth

## Slide 66: Basic ISL Diagram

## Slide 67: ISL Diagram
Right Way
Wrong Way

## Slide 68: Reduced Port Count

## Slide 69: Calculating Network Latency
All latency is measured in one direction
  1 meter = 5 nanoseconds of latency
  100 meters = 1 microsecond
  100 kilometers = 1 millisecond
  1000 kilometers = 10 milliseconds
LA to NY = ~2778 miles = ~4470 km = 44 milliseconds
Add 2 microseconds for each ASIC change made
Keep those cables short!

## Slide 70: Site to Site
FCIP – Fiber Channel over IP
FC Router – Fiber Channel Router (optional)
  Allows switches to talk, without sharing a fabric
  Zone from primary array to FCIP Router
  Zone from secondary array to FCIP Router
Lots of bandwidth is required
Keep network latency in mind
Allows site to site array based replication

## Slide 71: Site to Site Diagram

## Slide 72: Monitoring
Switches require monitoring too
Depending on Switch MRTG may be able to be used
Some 3rd party tools exist

## Slide 73: Virtualization Agenda
Major Platform Choices
Benefits
Pitfalls
Deciding Factors
Limits of Virtualization
Management Tools
Licensing

## Slide 74: Major Platform Choices
VMware
  ESX 1-3.5
  vSphere 4.0 – 4.1
    VMware announced 4.1 will be the last version with a host console 7/30/2010
  vSphere Hypervisor (ESXi) 4.0+
Hyper-V
  V1 and v2

## Slide 75: Benefits
Hardware Costs
Instant Server Deployment
Free Server Redundancy
  Live Migration – Hyper-V
  vMotion - VMware
Easy System Upgrades

## Slide 76: Pitfalls
Shared CPU
Shared Memory
Slow Disk Access times
Another layer of Management
Storage Path Flooding

## Slide 77: Deciding Factors
Disk IO
  IO Per Seconds
CPU Load
  CPU Usage
  Core Counts
  Processor Queuing
Memory Usage

## Slide 78: Virtualization Limits
vCPUs must be on the same physical socket
  Changed as of vSphere 4.1, requires advanced guest configuration
vMotion or Instant Failover requires hosts have like CPUs models
Hyper-V doesn’t include memory de-duplication

## Slide 79: Management Tools
VMware requires vCenter to manage a cluster
Hyper-V requires System Center Operations Manager
  SCOM can also manage ESX 3.5 or vSphere 4.0 servers (requires vCenter server)

## Slide 80: Thank You Sponsors!

## Slide 81: Denny Cherry
Please fill out the survey at http://speakerrate.com/mrdenny.
mrdenny@mrdenny.com
http://itke.techtarget.com/sql-server
http://twitter.com/mrdenny
Twitter
Contact Info
Blog